## Slide 1: OS Interaction with Cache Memories
Dr. Sohum Sohoni
School of Electrical and Computer Engineering
Oklahoma State University

## Slide 2: Outline
Technically ‘light’ talk- broad audience
Background terminology and one example of current work
Wild predictions about the future
  Many thanks to the National Science Foundation CNS #0720741
  Any views presented here are my own, and not reflective of the NSF’s views and policies

## Slide 3: Some Terminology
CPU Caches
  Miss rates
  Locality
  Prefetching
Context Switches
  ‘state’
  Working set or memory footprint
  Process queue

## Slide 4: Goal of Memory Hierarchy
Low latency, high bandwidth, high capacity, low cost
CPU
L1 Cache
L2 Cache
Main Memory
(System DRAM)
3GHz
Extremely fast bus
2 cycles
16 KB
Slower bus
2+7 = 9 cycles
512 KB
Much slower bus
300 cycles
512 MB

## Slide 5: What Happens in a Context Switch
Current process ‘state’ is saved
Scheduler is invoked
Next process is ‘brought in’
TLB’s are flushed
L1 cache may be flushed
New process executes for its time slice
Interrupt, state saved, scheduler …
Effective locality gets wiped out

## Slide 6: Effect of MultiProgramming
10ms
20ms
30ms
40ms
50ms
60ms
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
I/O
I/O
I/O
10ms
20ms
30ms
40ms
50ms
60ms
CPU
I/O
CPU
CPU
I/O
CPU
I/O
CPU
Memory pressure
Memory pressure

## Slide 7: Problem with MultiProgramming
Increasing multi-programming increases cache miss rates
Loss of locality of reference
Diminishing returns from multi-programming
Eventual thrashing
k

## Slide 8: Out of Context Prefetching
Reduce the negative effect of multi-programming on CPU cache performance
  Predict future context switches
  Prefetch the working set of the next process
Memory Pressure
Context Switch!
Time
Prefetch

## Slide 9: OOC Prefetching Picture
CPU
L1
L2
Main memory
OOC Prefetch

## Slide 10: Context Switch Prediction
Chart: Prediction Rate %
| CFS SPEC CPU - LAST | CFS SPEC OMP - LAST | O(1) SPEC OMP - FCM ORDER 7 | O(1) SPEC CPU - HYSTERESIS | O(1) SPEC OMP - HYSTERESIS | O(1) IDLE - HYSTERESIS | O(1) SPEC OMP - LAST | O(1) SPEC CPU - FCM ORDER 7 | O(1) IDLE - LAST | O(1) SPEC CPU - LAST | CFS SPEC CPU - HYSTERESIS | CFS IDLE - HYSTERESIS | O(1) IDLE - FCM ORDER 7 | CFS SPEC OMP - HYSTERESIS | CFS IDLE - LAST | O(1) SPEC OMP - FCM ORDER 3 | O(1) SPEC CPU - FCM ORDER 3 | O(1) IDLE - FCM ORDER 3 | CFS IDLE - FCM ORDER 3 | CFS SPEC CPU - FCM ORDER 7 | CFS SPEC OMP - FCM ORDER 7 | CFS SPEC CPU - FCM ORDER 3 | CFS SPEC OMP - FCM ORDER 3 | CFS IDLE - FCM ORDER 7
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24

## Slide 11: Miss Rate Improvement
Chart: Miss Rate Improvement
| mcf | bzip2 | gcc | soplex | xalancbmk | astar | sphinx3 | povray | h264ref
2048kb | 0.017323 | 0.097925 | 0.10498 | 0.12368 | 0.23722 | 0.26419 | 0.4759 | 0.48551 | 0.49355

## Slide 12: Thank you! Q and A